## Slide 1
Daniel Kirschen
Participating in Electricity Markets

## Slide 2: Perspective
Generator
Consumer
Retailer
Operator of a pumped-hydro plant

## Slide 3
Participating in Electricity Markets: The consumer’s perspective

## Slide 4: Consumer’s perspective
Microeconomic theory
VoLL
Low price elasticity of the demand
Demand reduction
Demand shifting

## Slide 5
Participating in Electricity Markets: The retailer’s perspective

## Slide 6: The retailer’s perspective
Sell energy to consumers, mostly at a flat rate (fixed price)
Buy energy in bulk:
  Spot market
  Contracts
Must forecast the load of its customers
Regional monopoly: traditional top-down forecasting
Retail competition: bottom-up forecasting
  Difficult problem: customer base changes
  Much less accurate than traditional load forecasting

## Slide 7: Fig. 4.1: Forecast demand, average forward purchase price and retail rate for the case of a flat retail tariff

## Slide 8: Fig. 4.2: Cost of forward purchases and retail hourly retail revenues for the case of a flat retail tariff

## Slide 9: Table 4.1: Retail operations over a 12-hour period for the case of flat retail tariff of 37 $/MWh
Hour | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | Totals
Load Forecast (MWh) | 221 | 219 | 254 | 318 | 358 | 370 | 390 | 410 | 382 | 345 | 305 | 256 | 3828
Forward Purchases (MWh) | 221 | 219 | 254 | 318 | 358 | 370 | 390 | 410 | 382 | 345 | 305 | 256 | 3828
Average Forward Prices ($/MWh) | 24.70 | 24.50 | 27.50 | 35.20 | 40.70 | 42.40 | 45.50 | 48.60 | 44.20 | 38.80 | 33.40 | 27.70 | 
Cost of Forward Purchases ($) | 5459 | 5366 | 6985 | 11194 | 14571 | 15688 | 17745 | 19926 | 16884 | 13386 | 10187 | 7091 | 144482
Hourly Revenues ($) | 8177 | 8103 | 9398 | 11766 | 13246 | 13690 | 14430 | 15170 | 14134 | 12765 | 11285 | 9472 | 141636
Hourly Profits ($) | 2718 | 2737 | 2413 | 572 | -1325 | -1998 | -3315 | -4756 | -2750 | -621 | 1098 | 2381 | -2846

## Slide 10: Fig 4.3: Forecast demand, average forward purchase prices and retail rate for the case of an on-peak/off-peak retail tariff

## Slide 11: Fig 4.4: Cost of forward purchases and retail hourly retail revenues for the case of an on-peak/off-peak retail tariff

## Slide 12: Table 4.2: Retail operations over a 12-hour period for an on-peak retail rate of 38 $/MWh and an off-peak retail rate of 36 $/MWh
Hour | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | Totals
Load Forecast (MWh) | 264 | 262 | 297 | 299 | 337 | 348 | 367 | 385 | 359 | 324 | 287 | 299 | 3828
Forward Purchases (MWh) | 264 | 262 | 297 | 299 | 337 | 348 | 367 | 385 | 359 | 324 | 287 | 299 | 3828
Average Forward Prices ($/MWh) | 24.70 | 24.50 | 27.50 | 35.20 | 40.70 | 42.40 | 45.50 | 48.60 | 44.20 | 38.80 | 33.40 | 27.70 | 
Cost of Forward Purchases ($) | 6521 | 6419 | 8168 | 10525 | 13716 | 14755 | 16699 | 18711 | 15868 | 12571 | 9586 | 8282 | 141821
Revenues ($) | 9504 | 9432 | 10692 | 11362 | 12806 | 13224 | 13946 | 14630 | 13642 | 12312 | 10906 | 10764 | 143220
Profits ($) | 2983 | 3013 | 2524 | 837 | -910 | -1531 | -2753 | -4081 | -2226 | -259 | 1320 | 2482 | 1399

## Slide 13: Fig 4.5: Imbalances between forward purchases and actual energy consumed and corresponding balancing costs

## Slide 14: Fig. 4.6: Spot prices and average forward prices

## Slide 15: Table 4.3: Retail operations over a 12-hour period for a flat retail rate of 37 $/MWh considering forecasting errors and implied spot market trades.
Hour | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | Totals
Forecast load | 221 | 219 | 254 | 318 | 358 | 370 | 390 | 410 | 382 | 345 | 305 | 256 | 3828
Forward energy purchases | 221 | 219 | 254 | 318 | 358 | 370 | 390 | 410 | 382 | 345 | 305 | 256 | 3828
Average forward price | 24.70 | 24.50 | 27.50 | 35.20 | 40.70 | 42.40 | 45.50 | 48.60 | 44.20 | 38.80 | 33.40 | 27.70 | 
Forward purchase costs | 5459 | 5366 | 6985 | 11194 | 14571 | 15688 | 17745 | 19926 | 16884 | 13386 | 10187 | 7091 | 144482
Actual loads | 203 | 203 | 259 | 328 | 413 | 401 | 415 | 450 | 377 | 355 | 331 | 268 | 4003
Imbalances | -18 | -16 | 5 | 10 | 55 | 31 | 25 | 40 | -5 | 10 | 26 | 12 | 175
Spot prices | 20.30 | 25.40 | 30.30 | 37.50 | 69.70 | 75.40 | 70.10 | 102.3 | 81.40 | 63.70 | 46.90 | 28.90 | 
Balancing costs | -365 | -406 | 152 | 375 | 3834 | 2337 | 1753 | 4092 | -407 | 637 | 1219 | 347 | 13568
Total hourly cost | 5094 | 4960 | 7137 | 11569 | 18405 | 18025 | 19498 | 24018 | 16477 | 14023 | 11406 | 7438 | 158050
Hourly revenues | 7511 | 7511 | 9583 | 12136 | 15281 | 14837 | 15355 | 16650 | 13949 | 13135 | 12247 | 9916 | 148111
Hourly profits | 2417 | 2551 | 2446 | 567 | -3124 | -3188 | -4143 | -7368 | -2528 | -888 | 841 | 2478 | -9939

## Slide 16
Participating in Electricity Markets:
The Generator’s Perspective

## Slide 17: Market Structure
Monopoly:
  Monopolist sets the price at will
  Must be regulated
Perfect competition:
  No participant is large enough to affect the price
  All participants act as “price takers”
Oligopoly:
  Some participants are large enough to affect the price
  Strategic bidders have market power
  Others are price takers
Monopoly
Oligopoly
Perfect Competition

## Slide 18: Perfect competition
All producers have a small share of the market
All consumers have a small share of the market
Individual actions have no effect on the market price
All participants are “price takers”

## Slide 19: Short run profit maximization for a price taker
Adjust production y until the marginal
cost of production is equal to the
price π
Production cost
Revenue
Independent of quantity produced because price taker
Output of one of the generators

## Slide 20: Example 4.2
Coal fired unit with minimum output 100 MW and
maximum output 500 MW

## Slide 21: Unit limits
?

## Slide 22: Piecewise linear cost curves

## Slide 23: Piecewise constant marginal cost curve

## Slide 24: Dispatch with piecewise curves

## Slide 25: Example 4.4

## Slide 26: Example 4.5

## Slide 27: Scheduling
Startup cost
Operating constraints
Environmental constraints
Other revenue opportunities
Forecasting errors

## Slide 28: Example 4.6
Hour | 1 | 2 | 3 | 4 | 5 | 6 | 7
Price [$/MWh] | 12.0 | 13.0 | 13.5 | 10.5 | 12.5 | 13.5 | 11.5
Generation [MW] | 257.7 | 450.0 | 500.0 | 100.0 | 353.8 | 500.0 | 161.5
Revenue [$] | 3,092 | 5,850 | 6,750 | 1,050 | 4,423 | 6,750 | 1,858
Running cost [$] | 3,063 | 5,467 | 6,123 | 1,235 | 4,240 | 6,123 | 1,933
Startup cost [$] | 600 | 0 | 0 | 0 | 0 | 0 | 0
Total cost [$] | 3,663 | 5,467 | 6,123 | 1,235 | 4,240 | 6,123 | 1,933
Profit [$] | -571 | 383 | 627 | -185 | 183 | 627 | -75
Cumulative profit [$] | -571 | -188 | 439 | 254 | 437 | 1,064 | 989

## Slide 29: Produce vs. Purchase
Minimize
subject to

## Slide 30: Example 4.7
L = 260 MW

## Slide 31: Bidding under perfect competition
Since there are lots of small producers, a change in bid causes a change in the order of the bids
If I bid at my marginal cost
  I get paid the market clearing price if marginal or infra-marginal producer
If I bid higher than my marginal cost
  I could become extra-marginal and miss an opportunity to sell at a profit
If I bid lower than my marginal cost
  I could have to produce at a loss
No incentive to bid anything else than marginal cost of production
Price
Quantity
supply
demand

## Slide 32: Marginal, infra-marginal, extra-marginal producers
Everything is sold at the market clearing price
Price is set by the “last” unit sold
Marginal producer:
  Sells this last unit
  Gets exactly its bid
Infra-marginal producers:
  Get paid more than their bid
  Collect economic profit
Extra-marginal producers:
  Sell nothing
No difference between centralized auction and bilateral market
Extra-marginal
Infra-marginal
Marginal producer
Price
Quantity
supply
demand

## Slide 33: Profit of an infra-marginal producer
π
Variable cost of producing energy
Economic profit
$/MWh
MWh

## Slide 34: Profit of an infra-marginal producer
Selling at marginal cost covers the variable cost of production
The difference between the market price and the marginal cost must pay for the fixed costs:
  No-load cost, startup cost
  Cost of building the plant
  Interest payments for the bank, dividends for the shareholders
A plant must therefore be infra-marginal often enough to cover its fixed costs
  Market price > marginal cost for enough hours of the year

## Slide 35: Profit of a marginal producer
Variable cost of producing energy
$/MWh
MWh
No economic profit!

## Slide 36: Profit of a marginal producer
If a marginal generator bids at its marginal cost, it makes no economic profit
  Covers only its variable cost of production
  Does not cover its fixed cost
Generators that are too often marginal or just below marginal will not recover their fixed costs if they bid at their marginal cost of production
  They must include part of their fixed costs in their offer price
  Their offer price is therefore higher than their marginal cost
  They can do it because competition is not perfect when the load is high because most generators are already producing

## Slide 37
Imperfect Competition

## Slide 38: Game theory and Nash equilibrium
Each firm must consider the possible actions of others when selecting a strategy
Classical optimization theory is insufficient
Two-person non-co-operative game:
  One firm against another
  One firm against all the others
Nash equilibrium:
  Given the action of its rival, no firm can increase its profit by changing its own action

## Slide 39: Imperfect Competition – Game theory
Nash equilibrium

## Slide 40: Bertrand model – Game in price

## Slide 41: Bertrand Competition
Example 1
  CA = 35 . PA $/h
  CB = 45 . PB $/h
Bid by A?
Bid by B?
Market price?
Quantity traded?
A
B
CA(PA)
CB(PB)
PA
PB
Inverse demand curve

## Slide 42: Bertrand Competition
Example 1
  CA = 35 . PA $/h
  CB = 45 . PB $/h
Marginal cost of A: 35 $/MWh
Marginal cost of B: 45 $/MWh
A will bid just below 45 $/MWh
B cannot bid below 45 $/MWh because it would lose money on every MWh
Market price: just below 45 $/MWh
Demand: 55 MW
PA = 55MW
PB = 0
A
B
CA(PA)
CB(PB)
PA
PB

## Slide 43: Bertrand Competition
Example 2
  CA = 35 . PA $/h
  CB = 35 . PB $/h
Bid by A?
Bid by B?
Market price?
Quantity traded?
A
B
CA(PA)
CB(PB)
PA
PB

## Slide 44: Bertrand Competition
Example 2
  CA = 35 . PA $/h
  CB = 35 . PB $/h
A cannot bid below 35 $/MWh because it would lose money on every MWh
A cannot bid above 35 $/MWh because B would bid lower and grab the entire market
Market price: 35 $/MWh
Paradox of Bertrand model of imperfect competition
  Identical generators: bid at marginal cost
  Non-identical generators: cheapest gets the whole market
Is this a realistic model of imperfect competition?
A
B
CA(PA)
CB(PB)
PA
PB

## Slide 45: Cournot model – Game in quantity
Cournot equilibrium

## Slide 46: Short run profit maximization with market power
is the total industry output
Production of generator i
Not zero because of market power

## Slide 47: Short run profit maximization with market power
is the price elasticity of demand
is the market share of generator i
< 1  at the optimum production, the marginal cost of generator i is less than the market price.

## Slide 48: Cournot competition: Example 1
CA = 35 . PA $/h
CB = 45 . PB $/h
Suppose PA= 15 MW and PB = 10 MW
Then D = PA + PB = 25 MW
π = 100 - D = 75 $/MW
RA= 75 . 15 = $ 1125 CA= 35 . 15 = $ 525
RB= 75 . 10 = $ 750 CB= 45 . 10 = $ 450
Profit of A = RA - CA = $ 600
Profit of B = RB - CB = $ 300
A
B
CA(PA)
CB(PB)
PA
PB

## Slide 49: Cournot competition: Example 1
Summary:
For PA=15MW and PB = 10MW, we have:
Price
Profit of A
Profit of B
Demand

## Slide 50: Cournot competition: Example 1
PA=15
PA=20
PA=25
PA=30
PB=10
PB=15
PB=20
PB=25

## Slide 51: Cournot competition: Example 1
PA=15
PA=20
PA=25
PA=30
PB=10
PB=15
PB=20
PB=25
Price decreases as supply increases
Profits of each affected by other
Complex relation between production and profits

## Slide 52: Let’s play the Cournot game!
PA=15
PA=20
PA=25
PA=30
PB=10
PB=15
PB=20
PB=25
Equilibrium solution!
A cannot do better without B doing worse
B cannot do better without A doing worse
Nash equilibrium

## Slide 53: Cournot competition: Example 1
Generators achieve price larger than their marginal costs
The cheapest generator does not grab the whole market
Generators balance price and quantity to maximize profits
Warning: price is highly dependent on modeling of demand curve and are thus often not realistic
Price
Profit of A
Profit of B
Demand
PA=25
PB=15
CA = 35 . PA $/h
CB = 45 . PB $/h

## Slide 54: Cournot competition: Example 2
CA = 35 . PA $/h
CB = 45 . PB $/h
…
CN = 45 . PN $/h
A is a “strategic” player
  i.e. with market power
The others are “the competitive fringe”
A
B
CA(PA)
CB(PB)
PA
PB
N
CN(PN)
PN
...

## Slide 55: Cournot competition: Example 2

## Slide 56: Cournot competition: Example 2

## Slide 57: Cournot competition: Example 2

## Slide 58: Other competition models
Supply functions equilibrium
  Bid price depends on quantity
Agent-based simulation
  Represent more complex interactions
Maximising short-term profit is not the only possible objective
  Maximizing market share
  Avoiding regulatory intervention

## Slide 59: Plants that do not burn fossil fuels
Nuclear power plants
Hydro-electric power plants

## Slide 60: Wind and solar generation
Intermittency and stochasticity
Government policies and subsidies
  Renewable portfolio standards
  Investment tax credits
  Production tax credits
  Feed-in tariffs
  Contracts for difference
  Renewable energy certificates
Effects on the market

## Slide 61: Self scheduling of storage

## Slide 62: Centralized scheduling of storage

## Slide 63: Example 4.12
Generating unit | (MW) minimum generation | (MW) maximum generation | ($/MWh) marginal cost | ($/h) fixed cost
1 | 0 | 500 | 10 | 500
2 | 100 | 350 | 25 | 250
3 | 0 | 200 | 50 | 100
1 | 0 | 500 | 10 | 500
2 | 100 | 350 | 25 | 250
3 | 0 | 200 | 50 | 100
Time period | 1 | 2 | 3
(MW) | 495 | 750 | 505
 | 1 | 2 | 3
 | 495 | 750 | 505

## Slide 64: Market settlement without storage
Hour | Price $/MWh |  | Unit 1 | Unit 2 | Unit 3
1 | 10 | Output (MWh) | 495 | 0 | 0
 |  | Revenue ($) | 4950 | 0 | 0
 |  | Cost ($) | 5450 | 0 | 0
 |  | Profit ($) | -500 | 0 | 0
2 | 25 | Output (MWh) | 500 | 250 | 0
 |  | Revenue ($) | 12500 | 6250 | 0
 |  | Cost ($) | 5500 | 6500 | 0
 |  | Profit ($) | 7000 | -250 | 0
3 | 50 | Output (MWh) | 500 | 0 | 5
 |  | Revenue ($) | 25000 | 0 | 250
 |  | Cost ($) | 5500 | 0 | 350
 |  | Profit ($) | 19500 | 0 | -100
 |  | Total profit ($) | 26,000 | -250 | -100
 |  | Total cost ($) | 23,300 |  | 

## Slide 65: Market settlement with a 1MW/10MWh battery
Hour | Price $/MWh |  | Unit 1 | Unit 2 | Unit 3 | Battery
1 | 10 | Output (MWh) | 496 | 0 | 0 | -1
 |  | Revenue ($) | 4960 | 0 | 0 | -10
 |  | Cost ($) | 5460 | 0 | 0 | 0
 |  | Profit ($) | -500 | 0 | 0 | -10
2 | 25 | Output (MWh) | 500 | 251 | 0 | -0.2
 |  | Revenue ($) | 12500 | 6275 | 0 | -5
 |  | Cost ($) | 5500 | 6525 | 0 | 0
 |  | Profit ($) | 7000 | -250 | 0 | -5
3 | 50 | Output (MWh) | 500 | 0 | 3.3 | 1
 |  | Revenue ($) | 25000 | 0 | 165 | 50
 |  | Cost ($) | 5500 | 0 | 265 | 0
 |  | Profit ($) | 19500 | 0 | -100 | 50
 |  | Total Profit ($) | 26,000 | -250 | -100 | 35
 |  | Total Cost ($) | 23,250 |  |  | 

## Slide 66: Market settlement with a 10MW/10MWh battery
Hour | Price $/MWh |  | Unit 1 | Unit 2 | Unit 3 | Battery
1 | 10 | Output (MWh) | 500 | 0 | 0 | -5
 |  | Revenue ($) | 5000 | 0 | 0 | -50
 |  | Cost ($) | 5500 | 0 | 0 | 0
 |  | Profit ($) | -500 | 0 | 0 | -50
2 | 25 | Output (MWh) | 500 | 251 | 0 | -1
 |  | Revenue ($) | 12500 | 6275 | 0 | -25
 |  | Cost ($) | 5500 | 6525 | 0 | 0
 |  | Profit ($) | 7000 | -250 | 0 | -25
3 | 10 | Output (MWh) | 500 | 0 | 0 | 5
 |  | Revenue ($) | 5000 | 0 | 0 | 50
 |  | Cost ($) | 5500 | 0 | 0 | 0
 |  | Profit ($) | -500 | 0 | 0 | 50
 |  | Total Profit ($) | 6,000 | -250 | 0 | -25
 |  | Total Cost ($) | 23,025 |  |  | 

## Slide 67: Flexible consumer’s perspective
Storage vs. flexible demand
Remunerating flexible demand
  Price-based
  Incentive-based

## Slide 68
Overall market perspective

## Slide 69: Offer curve
Chart: Offered Generation Capacity (MW)
Offer Price (US $/MWh)

## Slide 70: Variations in the price of electricity
Time
Load
00:00
06:00
12:00
18:00
24:00
Minimum load
Peak load

## Slide 71: Bid curve
Chart: Demand (MW)
Bid Price (US $/MWh)
Hour 11
Hour 3

## Slide 72: Market clearing
Chart: Demand (MW)
Offer Price (US $/MWh)
Hour 11
Hour 3

## Slide 73: ISO-NE Price-duration curve
Chart: Percentage of Hours
Average | 42.5629 | 42.5629

## Slide 74: AESO Price duration curve

## Slide 75: Price spikes because of increased demand
$/MWh
MWh
Normal peak
Small increases in peak demand cause
large changes in peak prices
Extreme
peak
πext
πnor

## Slide 76: Price volatility in the balancing mechanism

## Slide 77: Market power
A firm exercises market power when
  It reduces its output (physical withholding)
  or
  It raises its offer price (economic withholding)
in order to change the market price

## Slide 78: Example
If a firm sells 10 units, the market price is $15
  Option 1: offer to sell only 9 units and hope that the price rises enough to compensate for the loss of volume
  Option 2: offer to sell the 10th unit for a price higher than $15 and hope that this will increase the price
Profit increases if price rises sufficiently to compensate for possible decrease in volume

## Slide 79: Price spikes because of reduced supply
$/MWh
MWh
Normal peak
Small reductions in supply cause
large changes in peak prices
πext
πnor
Normal supply
Reduced supply

## Slide 80: When is market power more likely?
Imperfect correlation with market share
Demand does not have a high price elasticity
Supply does not have a high price elasticity:
  Highly variable demand
  All capacity sometimes used
  Output cannot be stored
Electricity markets are more vulnerable than others to the exercise of market power

## Slide 81: Mitigating market power
Increase elasticity
Increase number of competitors

## Slide 82: Increasing the elasticity reduces price spikes and the generators’ ability to exercise market power
$/MWh
MWh
πmin
πmax

## Slide 83: Increasing the elasticity of the demand
Obstacles
  Fixed prices
  Need for communication
  Need for storage (heat, intermediate products, dirty clothes)
Not everybody needs to respond to price signals to get substantial benefits
Increased elasticity reduces the average price
  Not in the best interests of generating companies
  Impetus will need to come from somewhere else

## Slide 84: Further comments on market power
ALL firms benefit from the exercise of market power by one participant
Unilaterally reducing output or increasing offer price to increase profits is legal
Collusion between firms to achieve the same goal is not legal
Market power interferes with the efficient dispatch of generating resources
  Cheaper generation is replaced by more expensive generation