## Slide 1: Generation Expansion
Daniel Kirschen

## Slide 2: The investor’s perspective
Generation is no longer a monopoly activity
  No captive customers
  Competing companies with other technologies
Will a new plant generate enough profit from the sale of energy to justify the investment?

## Slide 3: The consumer’s perspective
In a competitive environment, no generator is responsible for serving all the consumers
Will selling electrical energy be sufficiently profitable to encourage investors to build enough generation capacity?
Do investors need an extra incentive to build enough generation capacity?

## Slide 4
The Investor’s Perspective

## Slide 5: Example 1: Investing in a coal plant
Is it worth building a 500MW plant?
Assume a utilization factor of 80%
Assume average price of electrical energy is 32 $/MWh
Data for a coal plant

## Slide 6: Example 1 (continued)
Investment cost:
1021 $/kW x 500 MW = $510,500,000
Estimated annual production:
0.8 x 500 MW x 8760 h/year = 3,504,000 MWh
Estimated annual production cost:
3,504,000 MWh x 9419 Btu/kWh x 1.25 $/MBtu = $41, 255, 220
Estimated annual revenue:
3,504,000 MWh x 32 $/MWh = $112,128,000

## Slide 7: Example 1 (continued)
Total net cash flow over 30 years:
- $510,500,000 + 30 x $70,872,780 = $1,615,683,400
Is this plant profitable enough?

## Slide 8: Example 1 (continued)
Time value of money
  A dollar now is worth more to me than a dollar next year or
  How much interest should I be paid to invest my dollar for one year rather than spend it now?
  This interest should take inflation into account
Apply this concept to investments
  Calculate Internal Rate of Return (IRR) of net cash flow stream
    Standard accounting formula (use a spreadsheet)
    Gives more weight to profit in the early years than in the later years
  Example: IRR = 13.58%

## Slide 9: Example 1 (continued)
Is an IRR of 13.58% good enough?
  Compare it to the Minimum Acceptable Rate of Return (MARR) of the investor
  If IRR ≥ MARR  investment is OK
  If IRR < MARR investment is not worth making
How do firms set their MARR?
  Specializes in high risk investments
   set MARR high
  Specializes in low risk investments
   set MARR lower

## Slide 10: Example 1 (continued)
What are the risks?
  Average price of electricity may be less than 32 $/MWh
  Utilization factor may be less than 80%
Recalculate the IRR for various conditions
Utilization factor
MARR

## Slide 11: Example 2: CCGT Plant
Investment cost | 533 $/kW
Expected plant life | 30 years
Heat rate at rated output | 6,927 Btu/kWh
Expected fuel cost | 3.00 $/MBtu

## Slide 12: Example 2: CCGT Plant
Investment cost:
533 $/kW x 500 MW = $266,500,000
Annual production cost:
3,504,000 MWh x 6,927 Btu/kWh x 3.00 $/MBtu = $72,816,624
Annual production:
0.8 x 500 MW x 8760 hours/year = 3,504,000 MWh
Annual revenue:
3,504,000 MWh x 32 $/MWh = $ 112,128,000

## Slide 13: Example 2: CCGT Plant
Year | CCGT Plant Investment (A) | Coal Plant Investment (B) | CCGT Plant Production Cost (C) | Coal Plant Production Cost (D) | Incremental Net Cash Flow (A)-(B)+(C)-(D)
0 | $266,500,000 | $ 510,500,000 | 0 | 0 | - $ 244,000,000
1 | 0 | 0 | $ 72,816,624 | $ 41,255,220 | $ 31,561,404
2 | 0 | 0 | $ 72,816,624 | $ 41,255,220 | $ 31,561,404
3 | 0 | 0 | $ 72,816,624 | $ 41,255,220 | $ 31,561,404
… | … | … | … | … | …
30 | 0 | 0 | $ 72,816,624 | $ 41,255,220 | $ 31,561,404
 IRR =12.56%.

## Slide 14: Example 2: CCGT Plant

## Slide 15: Example 2: CCGT Plant

## Slide 16: Example 3: Wind farm
Investment cost | 919 $/kW
Expected plant life | 30 years
Heat rate at nominal output | 0
Expected fuel cost | 0
Initial investment cost :
919 $/kW x 100 MW = $ 91,900,000
Annual production:
0.35 x 100 MW x 8760 hours/year = 306,600 MWh
Annual revenue:
306,600 MWh x 32 $/MWh = $ 9,811,200

## Slide 17: Example 3: Wind farm
Year | Investment | Production | Production cost | Revenue | Net Cash Flow
0 | $ 91,900,000 | 0 | 0 | 0 | - $ 91,900,000
1 | 0 | 306,600 | 0 | $ 9,811,200 | $ 9,811,200
2 | 0 | 306,600 | 0 | $ 9,811,200 | $ 9,811,200
3 | 0 | 306,600 | 0 | $ 9,811,200 | $ 9,811,200
… | 0 | … | … | … | …
30 | 0 | 306,600 | 0 | $ 9,811,200 | $ 9,811,200
 IRR =10.08%.

## Slide 18: Retiring generation capacity
Once a plant has been built:
  Most of the investment cost becomes a sunk cost
  Sunk costs are irrelevant in further decisions
A plant will be retired if it no longer recovers its operating cost and is not likely to do so in the future
Examples:
  Operating cost increases because fuel cost increases
  Plant utilization and/or energy price decrease because cheaper plants become available
Decision based only on prediction of future revenues and costs
Technical fitness and lifetime are irrelevant

## Slide 19: Effect of a cyclical demand
Basic microeconomics:
  If demand increases or supply decreases (because plants are retired) prices will increase
  If prices increase, investment projects become more profitable
  New generating plants are built
Difficulties
  Demand for electricity is cyclical
  Electrical energy cannot be stored economically
  Must forecast utilization factor for each plant

## Slide 20: Load Duration Curve
PJM (Pennsylvania Jersey Maryland) system in 1999
Number of hours per year during which the demand exceeds a certain level

## Slide 21: Effect of cyclical demand
Peak load is much higher than average load
Total installed capacity must be much higher than average load
Cheap generators operate most of the time
More expensive generators operate during only a fraction of the time
Prices will be higher during periods of high demand
Competition will be limited during periods of high demand because most generators are already fully loaded

## Slide 22: Price duration curve
Actual peak price reached $1000/MWh for a few hours
PJM system, 1999

## Slide 23: What about the most expensive unit?
In a competitive market
  Market price set by marginal cost of marginal generator
  Infra marginal generators collect an economic profit because their marginal cost is less than the market price
  Economic profit pays the fixed costs
  Marginal generator does not collect any economic profit
  Marginal generator does not pay its fixed costs
Marginal producer
Price
Quantity
supply
demand
Infra-marginal
Economic
profit

## Slide 24: What about the most expensive unit?
Because of the cyclical demand, most units will be infra-marginal during part of the year
Most unit will therefore have an opportunity to recover their fixed costs
The unit that only runs a few hours a year to meet the peak demand is never infra-marginal
It must recover its costs by incorporating them in its price
  Must be recovered over a few hours only
  Prices are very high during these periods (price spikes)
  Possible because market is not competitive during these periods
  What if the yearly peak demand is lower than expected?

## Slide 25: Example 4: Retirement
Aging 50 MW plant
Heat rate: 12,000 BTU/kWh
Fuel cost: 3.00 $/MBTU
Fixed cost: $280,000 per year
Revenue required to cover the total operating cost:
Production [MWh] x bid [$/MWh] =
fixed cost [$] + production [MWh] x heat rate [Btu/kWh] x fuel cost [$/MBtu]

## Slide 26: Example 4: Retirement
Compare with the marginal cost of production of 36 $/MWh

## Slide 27
The consumer’s perspective

## Slide 28: Meeting the peak demand
In a competitive environment, there is no obligation on generating companies to build enough capacity to meet the peak demand
  The “regulatory compact” no longer applies to generators
Rely on price signals to encourage investments
What if no generation company wants to own the most expensive unit that runs only a few hours a year?
  Owning that plant is not very profitable and risky
Will there be enough generation capacity available to meet the reliability expectations?

## Slide 29: Consequences of not meeting the peak demand
Load must be shed (i.e. customers temporarily disconnected)
Cost of these interruptions: Value of Lost Load (VOLL)
VOLL is about 100 times larger than the average cost of electricity
Customers have a much stronger interest in having enough generation capacity than generators
Customers may be willing to pay extra to guarantee that there will be enough capacity available

## Slide 30: Capacity incentives
Advantages
  Capacity insurance policy: pay a little bit regularly to avoid a major problem
Disadvantages
  Less economically efficient behaviour
  How much should generators be paid per MW? Or
  How much capacity should be available?

## Slide 31: Capacity incentives
Capacity payments
  Pay generators a fixed rate per MW of capacity available
  Encourages them to keep available plants that don’t generate many MWh
Capacity market
  Regulator determines the generation capacity required to meet a reliability target
  Consumers must all “buy” their share of this capacity
  Generators bid to provide this capacity
  Price paid depends on how much capacity is offered
  Consider demand response in the capacity market