## Slide 1
Bob Iannucci, Ph.D.
Director, CyLab Mobility Research Center
Distinguished Service Professor, ECE
Ervin Teng
Ph.D. student, ECE
June, 2016
Modeling and Mitigating RF Vulnerabilities of Cellular Networks for UAS Communication

## Slide 2
Phone, sensor, actuator layer: devices have limited
Computing
Storage
Energy
Space
Cloud has unlimited
Computing
Storage
Energy
Space
Sense
Actuate
Network-as-participant
“Near-to-Near” (vs. peer-to-peer)
Today: latency too high
Future: embed virtualized, movable, real-time computing capability in the network
Cyber-physically enabled future network: Automated marshaling of computing
Physical World
Sense-Compute-Actuate Latency
Compute
Network for a Cyber-Physical World

## Slide 3: Open, Programmable Wireless Network: How do we get there?
Practical barrier: existing networks are closed and are resistant to study
Approach: telecom wireless network evolution has followed a somewhat different path than the evolution of the internet
Reality: current architecture evolved from circuit switching and assumption of wired last mile
  Characteristics of packet wireless are fundamentally different
  Architecture did not anticipate apps
Open instead of closed
Suggests need for cross-layer approach

## Slide 4: Clean-Sheet Design If we knew then what we know now…
Architecture
Compositional structure
  Dynamic trust
  Combined network + cloud
RAN-agnostic
  LTE, WiFi / IMS, LoRa, ...
  But RF-aware, power-aware
Applications
Emergency preparedness
  Rapid deployment
Smart cities
Air  ground (drones)
CROSSMobile Challenge: create and study an idealized open, programmable wireless network ... at interesting scale

## Slide 5: The CROSSMobile Project Today
The CROSSMobile™ Testbed
(GSM, LTE under experimental license)
Crowdsourced Smart Cities™
Adaptation and Cooperation
In-situ measurements and physics-based modeling
of environments
The Mobile Node
IoT: Low Power Computing & Comms
UAS + Cellular: “Holes in the Sky”
Wireless Emergency
Alerts
Indoor Positioning
Survivable Social Network

## Slide 6: Drones and the cyberphysical network

## Slide 7: UAS and Communications
Unmanned aerial systems (UAS) depend on communications for non-line-of-sight (NLOS) operation
  Telemetry / first-person-view video
  Command and control / navigation
Reliable coverage is needed
  Point-to-point: not pervasive; propagation unknown
  Satellite: equipment, power, latency limitations
  Proprietary terrestrial: expensive to build
  Hastily formed: propagation unknown
  Cellular: propagation known?

## Slide 8: Sometimes Aerial Cellular Coverage is Good
Plot of LTE signal strength over small village, as measured by cellular phone from a UAS at various altitudes. Signal strength from nearby commercial cell sites increases as altitude increases above obstructing terrain.
120m AGL
80m AGL
40m AGL

## Slide 9: ... But not Always
“Holes in the sky” are real and getting worse
Predictive models depend on knowledge of the environment and are computationally expensive and/or inaccurate
How can we avoid holes so as to maintain integrity of the RF link?
K. Daniel and C. Wietfeld, “Using Public Network Infrastructures for UAV Remote Sensing in Civilian Security Operations,” Homel. Secur. Aff., vol. 3, 2011.
Teng, E., Falcao, J. D., Dominguez, C. R., Mokaya, F., Zhang, P., & Iannucci, B. Aerial Sensing and Characterization of Three-Dimensional RF Fields. In Second International Workshop on Robotic Sensor Networks. Seattle, WA. 2015.

## Slide 10: Holes are Real and Attributable to Multiple Physical Effects
We seek to model the key physical effects that give rise to discrepancies between measured path loss and simple free-space path loss

## Slide 11: If We Had This Knowledge, How would we Apply It?
A. Network-Side
Modeling
(Re-) Deployment
Validation

## Slide 12: If We Had This Knowledge, How would we Apply It?
Predict intersection of flight path with areas of bad coverage (dynamic)
Dynamically re-plan flight path – see-and-avoid
Bad Coverage
B. UAS-Side

## Slide 13: Benefits
Mapping, Modeling and Mitigation of holes-in-the-sky will enable
  Networks to better serve aerial (UAS) clients
  UAS to anticipate RF propagation risks and pre-emptively mitigate their effects

## Slide 14: Our Approach
Obstacle Geometry
Cell Site Locations
Propagation Models
Navigation
Location of Holes-in-the-Sky
Network-side studies
Camera Imagery
Range Imaging
Companion project
UAS-side studies

## Slide 15: Measurement: Custom-Designed ProbeQuad
Geo-referenced readings corrected for vehicle speed (measurement reporting latency), angle-of-attack, rotation
½ wavelength 900MHz antenna
3D printed antenna stabilization gimbal
SBAS COTS GPS
Retractable landing gear
Laser rangefinder for terrain mapping
Consistency of measurements across 360° rotation to within 2dB

## Slide 16: Measurement: Ground Support System

## Slide 17: Experimental Venue: A Real, Physical Village at Camp Roberts
Above: 3D LIDAR-based model by Skye Corbett, USGS Left: SketchUp 3D model by CROSSMobile team

## Slide 18: Typical Experiments
Altitude
Imagery ©2016 AMBAG, DigitalGlobe, USDA Farm Service Agency, Map data ©2016 Google
Open Field Vertical Ladder Patterns
Vertical Dipole and Sectorized Antennas
Mock Village
Radial Patterns Vertical Dipole Antenna

## Slide 19: Effect 1: Two-Ray Interference
Beyond simple free-space path loss, we observe a clearly visible two-ray interference effect
Easy to model

## Slide 20: Effect 2: Fresnel Zone Incursions
Path loss and two-ray don’t account well for Fresnel Zone incursions
Here, the quad is flown below the roofline of an interfering building
Close in, blockage and diffraction must be modeled
Can approximate the geometry of obstacles (e.g., in this case, as a thin edge)

## Slide 21: Effect 3: Antenna Pattern
Omni antennas show deep null above
Sector antennas show deep nulls at various angles
Both manifest as large volumes in which signal strength will be minimal
vs.
(typ.) L-Com DS HGV906U 900 MHz Omni
(typ.) L-Com DS HG913P-120 900 MHz Sector
(blue) Horizontal (red) Vertical

## Slide 22: Combining the Models
Case A: Open field:
  Free-space loss and two-ray ground reflection effects only: within 3.4 dB of measured path loss
Case B: Obstructions:
  Knife-edge approximation and Fresnel diffraction: within 9 dB of measured path loss
  More sophisticated approximation of geometry can improve accuracy
For UAS:
  Approximate terrain and obstacle geometry using camera, other sensors
  Apply propagation modeling to estimate path loss

## Slide 23: Summary
Aerial coverage for cellular networks is questionable and getting worse
Holes-in-the-sky are attributable to multiple effects
Free-space path loss, two-ray reflection, Fresnel zone incursion and antenna pattern can be prioritized and modeled
Accurate modeling can lead to better performance:
  Network-side hole mitigations
  UAS-side mitigations
Modeling these based on scene analysis is showing promising results

## Slide 24
Thank you!