## Slide 1: Effects of the Transmission Network on Electricity Markets

## Slide 2: Introduction
No longer assume that all generators and loads are connected to the same bus
Need to consider:
  Congestion, constraints on flows
  Losses
Two forms of trading
  Bilateral or decentralized trading
  Pool or centralized trading

## Slide 3: Bilateral or decentralized trading
Transactions involves only buyer and seller
Agree on price, quantity and other conditions
System operator
  Does not get involved directly in trading
  Maintains balance and security of the system
    Buys or sells limited amounts of energy to keep load and generation in balance
    Limits the amount of power that generators can inject at some nodes if security cannot be ensured by other means

## Slide 4: Example of bilateral trading
G1 sold 300 MW to L1
G2 sold 200 MW to L2
Prices are a private matter
Quantities must be reported to system operator so it can check security
G1
G2
L1
L2
Bus A
Bus B
G3
Notes: Figure 6.1: Bilateral trading in a two-bus power system

## Slide 5: Example of bilateral trading
G1 sold 300 MW to L1
G2 sold 200 MW to L2
If capacity of corridor ≥ 500 MW  No problem
If capacity of corridor < 500 MW  some of these transactions may have to be curtailed
G1
G2
L1
L2
Bus A
Bus B
G3
Notes: Figure 6.1: Bilateral trading in a two-bus power system

## Slide 6: Which transaction should be curtailed?
Could use administrative procedures
  These procedures consider:
    Firm vs. non-firm transactions
    Order in which they were registered
    Historical considerations
  Do not consider relative economic benefits
  Economically inefficient
  Better to let the participants themselves decide what makes sense
Participants should purchase right to use the network when arranging a trade in energy
  Physical transmission rights
  Support actual transmission of power over a given link

## Slide 7: Physical transmission rights
G1 sold 300 MW to L1 at 30 $/MWh
G2 sold 200 MW to L2 at 32 $/MWh
G3 selling energy at 35 $/MWh
How much would L1 and L2 be willing to pay for transmission rights?
L2 should not pay more than 3 $/MWh for transmission rights
L1 should not pay more than 5 $/MWh for transmission rights
G1
G2
L1
L2
Bus A
Bus B
G3
Notes: Figure 6.1: Bilateral trading in a two-bus power system

## Slide 8: Problems with physical rights
Parallel paths
Market power

## Slide 9: Parallel paths
1
2
xA
xB
P
P
FB
FA
Notes: Fig. 6.2: Illustration of Kirchoff’s Voltage Law

## Slide 10: Parallel paths
1
2
3
C
A
B
D
Y
Z
Notes: Fig. 6.3: Active power flows on parallel paths

## Slide 11: Parallel paths
1
2
3
C
A
B
D
Y
Z
I
II
400 MW transaction between B and Y
Need to buy transmission rights on all lines
Notes: Fig. 6.3: Active power flows on parallel paths

## Slide 12: Parallel paths
1
2
3
C
A
B
D
Y
Z
I
II
400 MW transaction between B and Y
Not possible because exceeds capacities of lines 1-2 and 2-3
Notes: Fig. 6.3: Active power flows on parallel paths

## Slide 13: Counter-flows
1
2
3
C
A
B
D
Y
Z
200 MW transaction
between D and Z
III
IV
Notes: Fig. 6.3: Active power flows on parallel paths

## Slide 14: Resultant flows
1
2
3
C
A
B
D
Y
Z
The resultant flows are within the limits
Notes: Fig. 6.3: Active power flows on parallel paths

## Slide 15: Physical rights and parallel paths
Counter-flows create additional physical transmission rights
Economic efficiency requires that these rights be considered
Decentralized trading:
  System operator only checks overall feasibility
  Participants trade physical rights bilaterally
  Theory:
    Enough participants  market discovers optimum
  Practice:
    Complexity and amount of information involved are such that it is unlikely that this optimum can be found in time

## Slide 16: Physical rights and market power
G3 only generator at bus B
G3 purchases transmission rights from A to B
G3 does not use or resell these rights
Why?
Effectively reduces capacity from A to B
Allows G3 to increase price at B
“Use them or lose them” provision for transmission rights: difficult to enforce in a timely manner
G1
G2
L1
L2
Bus A
Bus B
G3

## Slide 17: Centralized or Pool Trading
Producers and consumers submit bids and offers to a central market
Independent system operator selects the winning bids and offers in a way that:
  Optimally clears the market
  Respects security constraints imposed by the network
No congestion and no losses: uniform price
Congestion or losses: price depend on location where generator or load is connected

## Slide 18: Borduria-Syldavia Interconnection
Perfect competition within each country
No congestion or losses within each country
  Single price for electrical energy for each country
  Price = marginal cost of production
DS= 1500 MW
Syldavia
DB= 500MW
Borduria
Notes: Fig. 6.7: Supply functions for the electrical energy markets of Borduria and Syldavia

## Slide 19: Borduria-Syldavia Interconnection
MW
$/MWh
13
1500
43
DS= 1500 MW
Syldavia
DB= 500MW
Borduria
10
15
500
MW
$/MWh
Notes: Fig. 6.7: Supply functions for the electrical energy markets of Borduria and Syldavia

## Slide 20: Borduria-Syldavia Interconnection
DB= 500MW
Borduria
DS= 1500 MW
Syldavia
Economic effects of an interconnection?
Notes: Fig. 6.7: Supply functions for the electrical energy markets of Borduria and Syldavia

## Slide 21: Can Borduria supply all the demand?
Generators in Syldavia can sell at a lower price than generators in Borduria
Situation is not tenable
Not a market equilibrium
DB= 500MW
Borduria
DS= 1500 MW
Syldavia
Notes: Fig. 6.7: Supply functions for the electrical energy markets of Borduria and Syldavia

## Slide 22: Market equilibrium
DB= 500MW
Borduria
DS= 1500 MW
Syldavia
Notes: Fig. 6.7: Supply functions for the electrical energy markets of Borduria and Syldavia

## Slide 23: Flow at the market equilibrium
DB= 500MW
Borduria
DS= 1500 MW
Syldavia
Notes: Fig. 6.7: Supply functions for the electrical energy markets of Borduria and Syldavia

## Slide 24: Graphical representation
= 567 MW
24.3 $/MWh
= 1433 MW
= 2000 MW
= 500 MW
= 1500 MW
24.3 $/MWh
= 933 MW
Supply curve for Syldavia
Supply curve for Borduria

## Slide 25: Constrained transmission
What if the interconnection can carry only 400 MW?
  PB = 500 MW + 400 MW = 900 MW
  PS = 1500 MW - 400 MW = 1100 MW
Price difference between the two locations
Locational marginal pricing or nodal pricing

## Slide 26: Graphical representation
= 1100 MW
35 $/MWh
= 900 MW
= 2000 MW
= 500 MW
= 1500 MW
= 400 MW
16 $/MWh
Notes: Fig. 6.10: Graphical representation of the effect of congestion on the Syldavian and Bordurian electricity markets.

## Slide 27: Summary

## Slide 28: Summary

## Slide 29: Winners and Losers
Winners:
  Bordurian generators
  Syldavian consumers
  Economies of both Borduria and Syldavia
    Better allocation of resources
Losers
  Bordurian consumers
  Syldavian generators
Congestion in the interconnection reduces these benefits

## Slide 30: Congestion surplus
Consumer payments:
Producers revenues:
Congestion or merchandising surplus:

## Slide 31: Congestion surplus
Notes: Fig. 6.11: Consumers’ payments (solid line) and generators’ revenue (dashed line) as a function of the flow on the interconnection between Borduria and Syldavia.

## Slide 32: Congestion surplus
Collected by the market operator in pool trading
Should not be kept by market operator in pool trading because it gives a perverse incentive
Should not be returned directly to network users because that would blunt the economic incentive provided by nodal pricing

## Slide 33: Centralized trading in larger networks
Independent System Operator (ISO) runs the market:
  Receives offers from the generators
  Forecasts the load at each node
  Dispatches the generation to meet the load at minimum cost taking the network constraints into account  Optimal Power Flow (OPF)
  Determines the price of electricity at each node
  Generators are paid the price of electricity at their node
  Consumers pay the price of electricity at their node

## Slide 34: Optimal Power Flow
Generating units and loads are not all connected to the same bus
The economic dispatch may result in unacceptable flows or voltages in the network
Network
A
B
C
D

## Slide 35: Optimal Power Flow – 2 bus example
A
B
100$/MWh
50 $/MWh
Maximum flow on each line: 100MW
PA
PB
PAMAX
PBMAX
LB
LA

## Slide 36: Acceptable ED solution
The solution of this (trivial) economic dispatch is:
A
B
LB = 200MW
LA = 100 MW
100 MW
100 MW
The flows on the lines are below the limit
The economic dispatch solution is acceptable
0 MW
300 MW

## Slide 37: Unacceptable ED solution
The solution of the economic dispatch is:
A
B
500 MW
0 MW
200 MW
200 MW
The resulting flows exceed their limit
The economic dispatch solution is not acceptable
LB = 400MW
LA = 100 MW

## Slide 38: OPF solution
In this simple case, the solution of the economic dispatch can be modified easily to produce acceptable flows.
A
B
300 MW
200 MW
100 MW
100 MW
LB = 400MW
LA = 100 MW
This could be done mathematically by adding the following inequality constraint:

## Slide 39: 3-bus example
1
2
3
B
A
450 MW
10 $/MWh
PA
PAMAX = 390MW
20$/MWh
PB
PBMAX= 150 MW
Economic dispatch:

## Slide 40: Flows resulting from the economic dispatch
1
2
3
B
A
450 MW
390MW
60MW
Assume that all the lines have the same reactance
Do these injection result in acceptable flows?
Fmax = 200MW
Fmax = 200MW
Fmax = 260MW

## Slide 41: Calculating the flows using superposition
Because we assume a linear model, superposition is applicable
1
60 MW
2
3
450 MW
390 MW
1
2
3
390 MW
390 MW
60 MW
1
2
3
60 MW

## Slide 42: Calculating the flows using superposition (1)
1
2
3
390 MW
390 MW
FA
FB
FA = 2 x FB because the path 1-2-3 has twice the reactance of the path 1-3
FA + FB = 390 MW
FA = 260 MW
FB = 130 MW

## Slide 43: Calculating the flows using superposition (2)
1
2
3
60 MW
60 MW
FD
FC
FC = 2 x FD because the path 2-1-3 has twice the reactance of the path 2-3
FC + FD = 60 MW
FC = 40 MW
FD = 20 MW

## Slide 44: Calculating the flows using superposition (3)
1
2
3
390 MW
390 MW
60 MW
1
2
3
60 MW
260 MW
130 MW
20 MW
40 MW
280 MW
1
60 MW
2
3
450 MW
390 MW
110 MW
170 MW
Fmax = 260 MW

## Slide 45: Correcting unacceptable flows
Must use a combination of reducing the injection at bus 1 and increasing the injection at bus 2 to keep the load/generation balance
Decreasing the injection at 1 by 3 MW reduces F1-3 by 2 MW
Increasing the injection at 2 by 3 MW increases F1-3 by 1 MW
A combination of a 3 MW decrease at 1 and 3 MW increase at 2 decreases F1-3 by 1 MW
To achieve a 20 MW reduction in F1-3 we need to shift 60 MW of injection from bus 1 to bus 2
280 MW
1
60 MW
2
3
450 MW
390 MW
Must reduce flow F1-3 by 20 MW

## Slide 46: Check the solution using superposition
1
2
3
330 MW
330 MW
120 MW
1
2
3
120 MW
220 MW
110 MW
40 MW
80 MW
260 MW
1
120 MW
2
3
450 MW
330 MW
70 MW
190 MW
Fmax = 260 MW

## Slide 47: Comments (1)
The OPF solution is more expensive than the ED solution
  CED = 10 x 390 + 20 x 60 = $5,100
  COPF = 10 x 330 + 20 x 120 = $5,700
The difference is the cost of security
  Csecurity = COPF - CED = $600
The constraint on the line flow is satisfied exactly
  Reducing the flow below the limit would cost more

## Slide 48: Comments (2)
We have used an “ad hoc” method to solve this problem
In practice, there are systematic techniques for calculating the sensitivities of line flows to injections
These techniques are used to generate constraint equations that are added to the optimization problem

## Slide 49: Pool trading in a three-bus example
1
2
3
C
A
B
D
50 MW
60 MW
300 MW

## Slide 50: Economic dispatch
1
2
3
C
A
B
D
50 MW
60 MW
300 MW
125 MW
285 MW
0 MW
0 MW

## Slide 51: Superposition
1
60 MW
2
3
300 MW
360 MW
1
60 MW
2
3
60 MW
1
2
3
300 MW
300 MW
Notes: Figure 6.14: Application of the superposition theorem to the calculation of the line flows in the three-bus system.

## Slide 52: Flows with economic dispatch
1
2
3
C
A
B
D
50 MW
60 MW
300 MW
125 MW
285 MW
0 MW
0 MW
156 MW
96 MW
204 MW

## Slide 53: Overload!
1
2
3
C
A
B
D
50 MW
60 MW
300 MW
125 MW
285 MW
0 MW
0 MW
156 MW
96 MW
204 MW
FMAX = 126 MW

## Slide 54: Correcting the economic dispatch
1
1 MW
2
3
1 MW
Additional generation at bus 2
0.6 MW
0.4 MW
Notes: Figure 6.16: Effect of an incremental change in the generation at bus 2.

## Slide 55: Parallel paths
1
2
xA
xB
P
P
FB
FA
Notes: Fig. 6.2: Illustration of Kirchoff’s Voltage Law

## Slide 56: Superposition
1
60 MW
2
3
300 MW
360 MW
156 MW
204 MW
96 MW
1
50 MW
2
3
50 MW
30 MW
20MW
1
10 MW
2
3
300 MW
310 MW
126 MW
184 MW
116 MW
Notes: Figure 6.17: Superposition of the redispatch of generation from bus 1 to bus 2 (B) on the economic dispatch (A) to produce a constrained dispatch that meets the constraints on line flows (C).

## Slide 57: Correcting the economic dispatch
1
1 MW
2
3
1 MW
Additional generation at bus 3
0.6 MW
0.4 MW
Notes: Figure 6.18: Effect of an incremental change in the generation at bus 3.

## Slide 58: Superposition
1
60 MW
2
3
300 MW
360 MW
156 MW
204 MW
96 MW
1
60 MW
2
3
225 MW
285 MW
126 MW
159 MW
66 MW
1
75 MW
2
3
75 MW
30 MW
45 MW
Notes: Figure 6.19: Superposition of the redispatch of generation from bus 1 to bus 3 (B) on the economic dispatch (A) to produce a constrained dispatch that meets the constraints on line flows (C).

## Slide 59: Cost of the dispatches
Economic dispatch: 2,647.50 $/h
Redispatch generator 2: 2,972.50 $/h
Redispatch generator 3: 2,835.00 $/h
Cost of security: 187.50 $/h

## Slide 60: Transmission constrained dispatch
1
2
3
C
A
B
D
50 MW
60 MW
50 MW
285 MW
0 MW
75 MW
126 MW
66 MW
159 MW
300 MW
This is the dispatch that the ISO will implement

## Slide 61: Calculating the prices at each node
Nodal price:
  Cost of supplying an additional MW of load without violating the security constraints
Start from the OPF solution

## Slide 62: Nodal prices
Node 1:
A is cheapest generator
1
2
3
C
A
B
D
50 MW
60 MW
50 MW
285 MW
0 MW
75 MW
126 MW
66 MW
159 MW
300 MW

## Slide 63: Nodal prices
Node 3
A is cheaper than D
Increasing A would overload line 1-2
D is cheaper than C
Increase D by 1 MW
1
2
3
C
A
B
D
50 MW
60 MW
50 MW
285 MW
0 MW
75 MW
126 MW
66 MW
159 MW
300 MW

## Slide 64: Nodal prices
Node 2
C is very expensive
Increasing A or D would overload line 1-2
?
1
2
3
C
A
B
D
50 MW
60 MW
50 MW
285 MW
0 MW
75 MW
126 MW
66 MW
159 MW
300 MW

## Slide 65: Nodal price at node 2
1
1 MW
2
3
1 MW
0.6 MW
0.4 MW
1
1 MW
2
3
0.2 MW
0.8 MW
1 MW
Notes: Figure 6.20: Incremental flows in the network due to an additional megawatt of load at bus 2 when this megawatt is produced at bus 1 (A) or at bus 3 (B).

## Slide 66: Nodal price at node 2
Increase generation at node 3 AND decrease generation at node 1
1
1 MW
2
3
Notes: Figure 6.21: Supplying an additional megawatt of load at bus 2 by increasing production at bus 3 and reducing it at bus 3.

## Slide 67: Nodal price using superposition
1
1 MW
2
3
0.2 MW
0.8 MW
1 MW
1
1 MW
2
3
1 MW
0.6 MW
0.4 MW
Notes: Figure 6.22: Application of the superposition theorem to the analysis of the conditions illustrated in Figure 6.17.

## Slide 68: Observations
Generators A and D are marginal generators because they supply the next MW of load at the bus where they are located
Generators B and C are not marginal
Unconstrained system: 1 marginal generator
m binding constraints: m+1 marginal generators
Prices at nodes where there is no marginal generator are set by a linear combination of the prices at the other nodes

## Slide 69: Summary for three-bus system
(= congestion surplus)

## Slide 70: Counter-intuitive flows
Power flows from high price to low price!
1
2
3
C
A
B
D
50 MW
60 MW
50 MW
285 MW
0 MW
75 MW
126 MW
66 MW
159 MW
300 MW
π2=11.25 $/MWh
π3=10.00 $/MWh
π1=7.50 $/MWh
Notes: Figure 6.24: Nodal marginal prices and flows in the three-bus system. Power in branch 2-3 flows from a higher marginal price to a lower marginal price.

## Slide 71: Counter-intuitive prices
Prices at nodes without a marginal generator can be higher or lower than prices at the other nodes
Nodal prices can even be negative!
Predicting nodal prices requires calculations
Strategically placed generators can control prices
Network congestion helps generators exert market power

## Slide 72: Counter-intuitive prices
Prices at nodes without a marginal generator can be higher or lower than prices at the other nodes
Nodal prices can even be negative!
Predicting nodal prices requires calculations
Strategically placed generators can control prices
Network congestion helps generators exert market power

## Slide 73: Nodal prices and market power
C desperate to produce
Bid 3 $/MWh
Other generators bid at marginal cost
1
2
3
C
A
B
D
50 MW
60 MW
Fmax =65 MW
300 MW

## Slide 74: Unconstrained dispatch
1
2
3
C
A
B
D
50 MW
60 MW
35 MW
285 MW
90 MW
0 MW
300 MW

## Slide 75: Constrained dispatch
1
2
3
C
A
B
D
50 MW
60 MW
32.5 MW
285 MW
7.5 MW
85 MW
300 MW
Fmax =65 MW

## Slide 76: Nodal prices
1
2
3
C
A
B
D
50 MW
60 MW
32.5 MW
285 MW
7.5 MW
85 MW
300 MW
Fmax =65 MW
π2 = 3.00 $/MWh
π3=12.00 $/MWh
π1=7.50 $/MWh
Low bid by C
Reduces price at bus 2
Increases price at bus 3
Very profitable for D!

## Slide 77: D increases its bid to 20 $/MWh
1
2
3
C
A
B
D
50 MW
60 MW
47.5 MW
285 MW
0 MW
77.5 MW
300 MW
Fmax =65 MW
π2 = -5.00 $/MWh
π3=20.00 $/MWh
π1=7.50 $/MWh
D takes advantage of the constraint on line 2-3
D’s output cannot be less than 77.5 MW
Can essentially bid what it wants

## Slide 78: Effect of losses on prices
D
1
2
G
Notes: Figure 6.25: Two-bus system illustrating the calculation of the marginal cost of losses

## Slide 79: Losses between Borduria & Syldavia
Minimization of the total cost
Notes: Fig. 6.26: Total generation cost in the Borduria-Syldavia interconnection as a function of the flow on the interconnector when the losses in this interconnector are and are not taken into consideration. The coefficient of the interconnector is . The resistances of the internal lines of the Bordurian and Syldavian networks have been neglected. The demands in Borduria and Syldavia are 500 MW and 1500 MW respectively.

## Slide 80: Mathematical Formulation of Nodal Pricing

## Slide 81: Introduction
Independent System Operator needs systematic method to calculate prices
Constrained optimization problem
  Maximization of global welfare
  Takes generator bids as representing marginal costs
Assume perfect competition

## Slide 82: One-bus network
Total demand of the consumers
Total production of the generators
Consumers’ benefit function
Producers’ cost function
Global welfare
Maximize
Subject to:
Suppliers’ profit
Quantity
Price
supply
demand
Consumers’ surplus
+
= Social or global welfare

## Slide 83: One-bus network
Lagrangian:
Optimality conditions:
Consumption and production increase
up to the point where marginal value =
marginal cost = price

## Slide 84: Network of infinite capacity with losses
: net injection at bus k
Network creates economic welfare by allowing trades between nodes with positive injections and nodes with negative injections
Benefits of consumers at node k
- Cost of producers at node k
: Global welfare

## Slide 85: Network of infinite capacity with losses
Welfare maximization:
Alternative formulations:
Assumes that:
Demands are insensitive to prices
Loads are constant
Hence consumers’ benefits are constant
Equivalent to Optimal Power Flow problem

## Slide 86: Network of infinite capacity with losses
Constraints:
No constraints on network flows because infinite capacity
Total generation = total load + losses or
Net injection = total losses in the branches of the network

## Slide 87: Why can we exclude the slack bus from L?
The power system is a closed system (conservation of energy)
or:
Let us assume that any change in injections at nodes
and consequent change in is compensated by a change in injection at node
Therefore

## Slide 88: Network of infinite capacity with losses

## Slide 89: Network of infinite capacity with losses
Nodal price at bus k is related to the nodal price at the slack bus
If the injection at a bus increases the losses, the price at that node will be less than the price at the slack bus
Penalizes the generators at that bus
Encourages consumers at that bus

## Slide 90: Network of finite capacity
Limits on line flows:
(Bus n is the slack bus)

## Slide 91: Network of finite capacity

## Slide 92: Assume that only line i is congested
Price at all buses (except slack bus) is affected by the congestion on any one
line.

## Slide 93: Solving this problem
As formulated, this is a non-linear optimization problem
Solution of non-linear problems is:
  Slow
  Not robust
    No convergence
    Solution may depend on the starting point
Need to linearize the problem
  Ignore losses (add them later as a correction)
  Linear expression for the flows as a function of the injections

## Slide 94: Power Flow
G
Bus k
To bus i
To bus j

## Slide 95: Power Flow Equations
For every node k in the network
: magnitude of voltage at buses k, i
: angle of voltage at buses k, i
: Real part of element k, i of the admittance matrix
: Imaginary part of element k, i of the admittance matrix

## Slide 96: Terms of the admittance matrix

## Slide 97: DC Power Flow
Neglect reactive power equations

## Slide 98: DC Power Flow
Neglect resistance of the branches

## Slide 99: DC Power Flow
Assume all voltage magnitudes = 1.0 p.u.

## Slide 100: DC Power Flow
Assume all angles are small
Flow in line i-j:

## Slide 101: Network of finite capacity: DC model
Line flows:
Line flow constraints:
Introduce the voltage angles as variables
Lagrangian function:
Power balance at each node
Power balance for the
whole system

## Slide 102: Network of finite capacity: DC model
(Slack at bus n)

## Slide 103: Implementation
m binding constraints  m+1 marginal generators
  Price at these buses determined using
  m+1 known prices
  n-m-1 unknown prices
  m unknown Lagrange multipliers
Use the second optimality condition to determine these prices and shadow prices:

## Slide 104: Implementation
K: set of buses where the price is known
U: set of buses where the price is unknown
(Slack at bus n)

## Slide 105: Example
1
2
3
C
A
B
D
π2 = ?
π3=10.00 $/MWh
π1=7.50 $/MWh
Marginal generators at buses 1 and 3:
Congested lines
Notes: Figure 6.24: Nodal marginal prices and flows in the three-bus system. Power in branch 2-3 flows from a higher marginal price to a lower marginal price.

## Slide 106: Example
1
2
3
C
A
B
D
π2 = ?
π3=10.00 $/MWh
π1=7.50 $/MWh
Notes: Figure 6.24: Nodal marginal prices and flows in the three-bus system. Power in branch 2-3 flows from a higher marginal price to a lower marginal price.

## Slide 107: Example
Choose bus 3 as the slack bus

## Slide 108: Example

## Slide 109: Example
=10.00 $/MWh
=7.50 $/MWh

## Slide 110: Interpretation of Lagrange multipliers
Marginal cost of the constraint on line i-j

## Slide 111: AC Modeling
DC power flow:
  Only models the flows of active power
  Does not model the voltage magnitudes
  Ignores constraints on voltage magnitudes
  Considers only the active power injections
Because of these inaccuracies, operators impose conservative limits on line flows
Hinders market efficiency
However, full AC modeling is not yet feasible
Reliably clearing the market is more important than economic efficiency

## Slide 112: Financial Transmission Rights

## Slide 113: Managing transmission risks
Congestion and losses affect nodal prices
Additional source of uncertainty and risk
Market participants seek ways of avoiding risks
Need financial instruments to deal with nodal price risk

## Slide 114: Contracts for difference
Centralized market
  Producers must sell at their nodal price
  Consumers must buy at their nodal price
Producers and consumers are allowed to enter into bilateral financial contracts
  Contracts for difference

## Slide 115: Example of contract for difference
Contract between Borduria Power and Syldavia Steel
  Quantity: 400 MW
  Strike price: 30 $/MWh
Other participants also trade across the interconnection
400 MW
Borduria
400 MW
Syldavia Steel
Syldavia
Borduria Power

## Slide 116: No congestion  market price is uniform
Borduria Power sells 400 at 24.30  gets $9,720
Syldavia Steel buys 400 at 24.30 pays $9,720
Syldavia Steel pays 400 (30 - 24.30) = $2,280 to Borduria Power
Syldavia Steel net cost is $12,000
Borduria power net revenue is $12,000
They have effectively traded 400 MW at 30 $/MWh$
400 MW
Borduria
400 MW
Syldavia Steel
Syldavia
Borduria Power
πB = 24.30 $/MWh
πS = 24.30 $/MWh

## Slide 117: Congestion  Locational price differences
Borduria Power sells 400 at 19.00  gets $7,600
Syldavia Steel buys 400 at 35.00  pays $14,000
Borduria Power expects 400 (30 -19) = $4,400 from Syldavia Steel
Syldavia Steel expects 400 (35 -30) = $2,000 from Borduria Power
Shortfall of $6,400
Basic contracts for difference break down with nodal pricing!
400 MW
Borduria
400 MW
Syldavia Steel
Syldavia
Borduria Power
πB = 19 $/MWh
πS = 35 $/MWh

## Slide 118: Financial Transmission Rights (FTR)
Observations:
  Shortfall in contracts for difference is equal to congestion surplus
  Congestion surplus is collected by the system operator
Concept:
  System operator sells financial transmission rights to users
  FTR contract for F MW between Borduria and Syldavia entitles the owner to receive:
  Holders of FTRs are indifferent about where they trade energy
  System operator collects exactly enough money in congestion surplus to cover the payments to holders of FTRs

## Slide 119: Example of Financial Transmission Rights
Contract between Borduria Power and Syldavia Steel
  Quantity: 400 MW
  For delivery in Syldavia (i.e. at the nodal price in Syldavia)
  Strike price: 30 $/MWh
To cover itself against location price risk, Borduria Power purchases 400 MW of financial transmission rights from the System Operator
400 MW
Borduria
400 MW
Syldavia Steel
Syldavia
Borduria Power

## Slide 120: Example of Financial Transmission Rights
Borduria Power sells 400 at 19.00  gets $7,600
Syldavia Steel buys 400 at 35.00  pays $14,000
The system operator collects 400 (35 -19) = $ 6,400 in congestion surplus
Borduria Power collects 400 (35 -19) = $6,400 from the system operator
Borduria Power pays Syldavia Steel 400 (35 -30) = $2,000
Syldavia Steel net cost is $12,000
Borduria power net revenue is $12,000
400 MW
Borduria
400 MW
Syldavia Steel
Syldavia
Borduria Power
πB = 19 $/MWh
πS = 35 $/MWh
400 MW
The books balance!

## Slide 121: Financial transmission rights (FTR)
FTRs provide a perfect hedge against variations in nodal prices
Auction transmission rights for the maximum transmission capacity of the network
  The system operator cannot sell more transmission rights than the amount of power that it can deliver
  If it does, it will lose money!
  System Operator has no incentive to increase congestion
Proceeds of the auction help cover the investment costs of the transmission network
Users of FTRs must estimate the value of the rights they buy at auction

## Slide 122: Financial transmission rights
FTRs are defined from point-to-point
No need for a direct branch connecting directly the points between which the FTRs are defined
Market participants do not need to be concerned about how the power flows from one location to another
  That’s the system operator’s job
FTRs automatically factor in the effect of Kirchoff’s voltage law

## Slide 123: Another example of FTRs
1
2
3
C
A
B
D
50 MW
60 MW
50 MW
285 MW
0 MW
75 MW
126 MW
66 MW
159 MW
300 MW
π2=11.25 $/MWh
π3=10.00 $/MWh
π1=7.50 $/MWh
Consumer at bus 3:
CFD with generator at bus 1
  100 MW at 8$/MWh
  Reference price: node 1
Purchased FTR for 100 MW from node 1 to node 3
Notes: Figure 6.24: Nodal marginal prices and flows in the three-bus system. Power in branch 2-3 flows from a higher marginal price to a lower marginal price.

## Slide 124: Settlement
Consumer pays 100 MW x 10.00 $/MWh = $1,000 for extracting 100 MW at bus 3.
Generator collects 100 MW x 7.50 $/MWh = $750 for injecting 100 MW at bus 1.
Consumer pays 100 x (8.00 –7.50) = $50 to the generator to settle the contract for difference.
Consumer collects 100 x (10.00 –7.50) = $250 from the system operator for the FTRs
Consumer effectively pays $800 for 100 MW, which is equivalent to a price of 8.00 $/MWh.

## Slide 125: Simultaneous feasibility
The system operator should not sell more FTRs than the transmission network can physically handle
The set of FTRs that it sells must meet the “simultaneous feasibility test”
  If flows corresponding to these FTRs are actually implemented, the system operating limits should be respected.
If this test is not satisfied, the system operator will not collect enough congestion surplus to cover its FTR obligations

## Slide 126: Transmission constrained dispatch
1
2
3
C
A
B
D
50 MW
60 MW
50 MW
285 MW
0 MW
75 MW
126 MW
66 MW
159 MW
300 MW
This dispatch is feasible and
uses the maximum transmission capacity

## Slide 127: Maximum net feasible injections
1
2
3
285 MW
60 MW
225 MW

## Slide 128: Feasible FTR combination A
1
2
3
285 MW
60 MW
225 MW
60MW
225 MW

## Slide 129: Feasible FTR combination B
1
2
3
285 MW
60 MW
225 MW
60MW
285 MW

## Slide 130: Feasible FTR combination C
1
2
3
285 MW
60 MW
225 MW
50MW
275 MW
10MW

## Slide 131: Settlement with these FTR combinations
 | Transmission rights |  |  | Settlement |  |  | 
Combination | From bus | To bus | Amount [MW] | From bus price [$/MWh] | To bus price [$/MWh] | Revenue [$] | Total [$]
A | 1 | 3 | 225 | 7.50 | 10.00 | 562.50 | 787.50
 | 1 | 2 | 60 | 7.50 | 11.25 | 225.00 | 
B | 1 | 3 | 285 | 7.50 | 10.00 | 712.50 | 787.50
 | 3 | 2 | 60 | 10.00 | 11.25 | 75.00 | 
C | 1 | 3 | 275 | 7.50 | 10.00 | 687.50 | 787.50
 | 1 | 2 | 10 | 7.50 | 11.25 | 37.50 | 
 | 3 | 2 | 50 | 10.00 | 11.25 | 62.50 | 
These are settlements for financial contracts, not the physical injections
These combinations of FTRs use all the available transmission capacity

## Slide 132: Congestion surplus
(= congestion surplus)
Equal to the total value of the FTRs

## Slide 133: Sensitivity to flow limits
1
2
3
C
A
B
D
50 MW
60 MW
50 MW
285 MW
0 MW
75 MW
126 MW
66 MW
159 MW
300 MW
π2=11.25 $/MWh
π3=10.00 $/MWh
π1=7.50 $/MWh
Notes: Figure 6.24: Nodal marginal prices and flows in the three-bus system. Power in branch 2-3 flows from a higher marginal price to a lower marginal price.

## Slide 134: Reduced limit on line 2-3
1
2
3
C
A
B
D
50 MW
60 MW
47.5 MW
285 MW
0 MW
77.5 MW
125 MW
65 MW
157.5 MW
300 MW
Π2= 5.00 $/MWh
π3=10.00 $/MWh
π1=7.50 $/MWh
Notes: Figure 6.24: Nodal marginal prices and flows in the three-bus system. Power in branch 2-3 flows from a higher marginal price to a lower marginal price.

## Slide 135: Value of FTRs
 | Transmission rights |  |  | Settlement |  |  | 
Combination | From bus | To bus | Amount [MW] | From bus price [$/MWh] | To bus price [$/MWh] | Revenue [$] | Total [$]
A | 1 | 3 | 225 | 7.50 | 10.00 | 562.50 | 412.50
 | 1 | 2 | 60 | 7.50 | 5.00 | -150.00 | 
B | 1 | 3 | 285 | 7.50 | 10.00 | 712.50 | 412.50
 | 3 | 2 | 60 | 10.00 | 5.00 | -300.00 | 
C | 1 | 3 | 275 | 7.50 | 10.00 | 687.50 | 412.50
 | 1 | 2 | 10 | 7.50 | 5.00 | -25.00 | 
 | 3 | 2 | 50 | 10.00 | 5.00 | -250.00 | 

## Slide 136: Observations
Price at bus 2 is lower than prices at bus 1 and 3 because increasing the load at bus 2 would reduce the cost of congestion
Some of the FTRs have a negative value
This means that the owners of these FTRs have to pay the system operator!

## Slide 137: Another FTR example
1
2
3
C
A
B
D
50 MW
60 MW
47.5 MW
285 MW
0 MW
77.5 MW
125 MW
65 MW
157.5 MW
300 MW
Π2= 5.00 $/MWh
π3=10.00 $/MWh
π1=7.50 $/MWh
Consumer at bus 2:
CFD with generator at bus 1
  60 MW at 8$/MWh
  Reference price: node 1
Purchased FTR for 60 MW from node 1 to node 2
Notes: Figure 6.24: Nodal marginal prices and flows in the three-bus system. Power in branch 2-3 flows from a higher marginal price to a lower marginal price.

## Slide 138: Settlement
Consumer pays 60 MW x 5.00 $/MWh= $300
Generator collects 60 MW x 7.50 $/MWh = $450
Consumer pays 60 x (8.00 –7.50) = $30 to the generator to settle the contract for difference.
Consumer pays 60 x (7.50 – 5.00) = $150 to the system operator for the FTRs
Consumer thus pays a total of $480, which is equivalent to the 8.00 $/MWh strike price in its contract for difference.

## Slide 139: Congestion surplus
 | Bus 1 | Bus 2 | Bus 3 | 
Load | 50 | 60 | 300 | 
Generation | 332.5 | 0 | 77.5 | 
Price | 7.50 | 5.00 | 10.00 | 
$ to generators | 2,493.75 | 0 | 775 | 3268.75
$ from loads | 375 | 300 | 3000 | 3675
Net $ | -2118.75 | 300 | 2225 | $406.25
Less than the $412.50 total value of the FTRs
Why?
Because the system operator was not able to deliver the full transmission capacity that it assumed when it sold the FTRs

## Slide 140: Problems with financial transmission rights
There are many possible point-to-point transmission rights
Difficult to assess the value of all possible rights
Difficult to set up a market for point-to-point transmission rights

## Slide 141: Flowgate rights (FGRs)
Observation:
  Typically, only a small number of branches are congested
Concept:
  Buy transmission rights only on those lines that are congested
  Theoretically equivalent to point-to-point rights
Advantage:
  Fewer rights need to be traded
  More liquid market
Difficulty:
  Identify the branches that are likely to be congested

## Slide 142: Flowgate rights
FTRs based on differences in nodal prices
  Differences in locational marginal costs
  Lagrange multipliers
FGRs based on marginal cost of flow constraints
  Lagrange multipliers
Value of FGR: x amount

## Slide 143: FTRs vs. FGRs
Fewer potentially congested lines than point-to-point combinations of FTRs
More liquid market for FGRs than FTRs
Hard to predict the value of point-to-point FTRs
Hard to predict when a particular line will be congested
Must understand operation of the network when dealing with FGRs